## Slide 1
EIP Protocol: Overview (v0.1)
Our communication is based on a pub/sub system with a star topology with a broker in the middle. Typically, it will be implemented with MQTT but that is not fixed. As such, we can subscribe for topics and topic filters, we can unsubscribe and we can publish messages.
Open Issue: it is unclear if we want to use more advanced MQTT features like QoS level, will message, etc.
Messages consist of a topic and data. Depending on the packet type, data may be empty. The basic message format is:
(“<topic>”, “<data>”), which <topic> and <data> both being strings.
Messages are distinguished by their topics, i.e., the message type is encoded into the topic. The topic format is:
eip://<domain>/<object>/<message type>/<type dependent>
We have 6 different message types:
HEART : a heartbeat message
START : a message requesting an object to start sending some (stream of) data
STOP: : a message requesting an object to stop sending some (stream of) data
DATA : a data message
DO : a command message
DONE : a command response

## Slide 2
EIP Protocol: Message Format (1/2)
HEART:
Topic = eip://<domain>/<object>/HEART
Data = empty OR twin ID (in case of a physical object joining)
E.g.: (“eip://uni-due.de/es/twin1/HEART”, “”)
START:
Topic = eip://<domain>/<object>/START/<data id>
Data = topic specifying object that is interested in data
E.g.: (“eip://uni-due.de/es/twin1/START/light”, “eip://uni-due.de/es/twin2”)
STOP:
Topic = eip://<domain>/<object>/STOP/<data id>
Data = topic specifying object that is interested in data
E.g.: (“eip://uni-due.de/es/twin1/STOP/light”, “eip://uni-due.de/es/twin2”)
DATA:
Topic = eip://<domain>/<object>/DATA/<data id>
Data = value, encoded as string
E.g.: (“eip://uni-due.de/es/twin1/DATA/light”, “30.6”)

## Slide 3
EIP Protocol: Message Format (2/2)
DO:
Topic = eip://<domain>/<object>/DO/<command specific>
Data = command specific
DONE:
Topic = eip://<domain>/<object>/DONE/<command specific>
Data = command specific
We currently support two commands:
TURN_ON:
Topic = eip://<domain>/<object>/DO/<SET>/<service>
Data = “1”
E.g.: (“eip://uni-due.de/es/twin1/DO/SET/led”, “1”)
TURN_OFF:
Topic = eip://<domain>/<object>/DO/<SET>/<service>
Data = “0”
E.g.: (“eip://uni-due.de/es/twin1/DO/SET/led/1”, “0”)
A response would lead to the following message being published:
(“eip://uni-due.de/es/twin1/DONE/SET/led/2”, “0”)
Currently it is predefined for each command if we expect a response or not. In the future this might be selectable. Turn on / off do not expect responses (the given response is provided as an example).
Open Question: we could also send a DATA message instead of a DONE message, indicating the change of state of the object resulting from the command. Would that be better / equal?

## Slide 4
EIP Protocol: Operations
Sending a heartbeat:
pub HEART message every x ms (x is deployment specific)
Sending data:
pub DATA message
Requesting data reception:
sub DATA topic
pub START message
Cancelling data reception:
pub STOP message
unsub DATA topic
Sending a command without response:
pub DO message
Sending a command with response from A to B:
A: sub DONE topic
A: pub DO message
B: pub DONE message

## Slide 5
EIP Protocol: Operations
HEARTBEATS or MQTT KeepAlive + Will ?
Note that we may not need HEARTBEATS after all if we do not deliver more information in them than just presence.
MQTT provides a keepAlive mechanism, which could in combination with a will message be used to notify twins when another one is leaving.
This should be hidden in the Broker!
A will message then could look like:
eip://uni-due.e/es/twin1/LOST
Thus, a Source could subscribe for this message at its CommunicationEndpoint and could remove this client from its client list when it receives its message.
A broker then needs to offer an interface for twins to register their own will message, right?

## Slide 6
EIP Protocol: Operations
An object A joining the system of broker B:
A: pub HEART message with twin ID X
B: starting specified twin X, providing it with object A’s ID
X: pub DO/BIND message
Or should we have a special JOIN message?
An object trying to identify all objects in Room BC105:
sub <domain>/+/DATA/location/bc105
Should we encode changes in the HEART message?
Should we provide the ability to request a description?
We could add the ability to ask for a single data update, i.e., a shortcut for sending START, getting one update and sending STOP again. Example:
eip://uni-due.e/es/twin1/GET/temperature
OR
eip://uni-due.e/es/twin1/ONCE/temperature

## Slide 7
Twin A
Twin B
Broker C
Device D
pub <eip://C/A/HEART>
pub <eip://C/B/HEART>
pub <eip://C/A/HEART>
pub <eip://C/B/HEART>
pub <eip://C/A/HEART>
pub <eip://C/B/HEART>
…
…
EIP Protocol: Basic Device Operation (Heartbeats)

## Slide 8
Twin A
Twin B
Broker C
Device D
pub <eip://C/B/DATA/d1>
sub <eip://C/B/DATA/d1>
pub <eip://C/B/DATA/d1>
<eip://C/B/DATA/d1>
…
EIP Protocol: Getting access to data that is sent continuously

## Slide 9
Twin A
Twin B
Broker C
Device D
sub <eip://C/B/DATA/d1>
sub <eip://C/A/HEART>
<eip://C/B/START/d1>
pub <eip://C/B/START/d1>
pub <eip://C/B/DATA/d1>
<eip://C/B/DATA/d1>
pub <eip://C/B/STOP/d1>
<eip://C/B/STOP>
Getting access to data that needs to be requested
unsub <eip://C/A/HEART>
stop sending data
start sending data

## Slide 10
Twin A
Twin B
Broker C
Device D
sub <eip://C/B/DATA/d1>
sub <eip://C/A/HEART>
<eip://C/B/START/d1>
pub <eip://C/B/START/d1>
pub <eip://C/B/DATA/d1>
<eip://C/B/DATA/d1>
pub <eip://C/A/HEART>
<eip://C/A/HEART>
Getting access to data that needs to be requested
start timeout
timeout fired
unsub <eip://C/A/HEART>
stop sending data
start sending data
…
…
…
…

## Slide 12
Twin A
Twin B
Broker C
Device D
sub <eip://C/B/DATA/d1>
sub <eip://C/A/HEART>
pub <eip://C/D/HEART>
pub <eip://C/B/START/d1>
pub <eip://C/B/DATA/d1>
<eip://C/B/DATA/d1>
pub <eip://C/A/HEART>
<eip://C/A/HEART>
Getting access to data that needs to be requested